Assignment 3.02: Electrostatic Fields and Potentials
1. A particle has a charge of +5 nC.
  1. Sketch the electric field of the charge.

  1. What is the electric field due to the charge a distance of 5 cm to the right of the charge (magnitude and direction)?

  1. What is the electric potential at the same point?

  1. A 2 nC charge is placed 5cm to the right of the original charge. What is its electrical potential energy?

In a hydrogen atom, the ionization energy is 2.18 × 10−18 J. Assuming an electron orbits the proton like a planet orbits the sun, what is the distance between the electron and the proton?

1. Two parallel metal plates are separated by a distance of 0.05 m. They are connected to a 1000V potential difference.
  1. Sketch the electric field between the plates:

  1. What is the magnitude of the electric field between the plates?

  1. A small piece of dust, m=3.5x10-6 kg, happened to be stuck to the positive plate before it was turned on. It has a charge of 1.5 x 10-15 C. Ignoring air resistance, how fast would the piece of dust be traveling when it strikes the positive plate?

During fair weather, the electric field near the surface of the earth is approximately 150 N/C, pointing downward. An adult spider of a certain species has a mass of 0.15 grams. If a spider releases a single strand of silk with a linear charge density of -1x10-6 C/m, how long would a strand need to be in order to lift the spider?

Electric eel sometimes hunt by using electricity to stun their prey. Larger electric eels can produce voltages of 650V at a distance of 1 meters away. What is the magnitude of the electric field produced by the eel?