Assignment #8.05: Angular Velocity and Acceleration

1. A man pushes a wheelbarrow a distance of 25m. The wheel has a radius of 0.1 m.
  1. What is the angular displacement of the wheel?

  1. How many rotations does the wheel make?

A car travels at 60 mph (26.8224 m/s). Its wheels have a radius of 0.23 m. What is the angular velocity of the wheel?

A train starts from a stop and accelerates forward at a rate of 0.24 m/s2. The wheels have a radius of 0.5 m. What is the angular acceleration of the wheels?

1. A marble rolls to the right along a flat surface at a constant speed of 0.3 m/s. The marble has a radius of 0.01m.
  1. What is the angular velocity of the marble?

  1. How far does the marble roll in 10 seconds?

  1. What is the angular displacement of the marble after 10 seconds?

1. Dorian is riding his bicycle, which has 26-inch (66.04 cm) diameter wheels. He starts from a stop and accelerates to a speed of 15 m/s in 10 seconds.
  1. What is Dorian's (linear) acceleration?

  1. What is the angular acceleration of the wheels?

  1. What is the final angular speed of the wheels?

El Paso, Texas, is located at 31.7619°N. Yellowknife, Northwest Territories, Canada, is located at 62.4540°N.
  1. Is a person in El Paso traveling with greater, lesser, or the same angular velocity as a person at the equator?

_____Greater	_____ Lesser	_____The Same
   Justify your answer.

  1. Is a person in El Paso traveling with greater, lesser, or the same linear velocity as a person in Yellowknife?

_____Greater	_____ Lesser	_____The Same
   Justify your answer.

  1. The earth spins with an angular velocity of 7.2921159 × 10−5 rad/s, and its equatorial radius is 6.371x106 m. What is the speed that a person at the equator is moving due to the rotation of the earth?

  1. What is the speed that a person in El Paso is moving due to the rotation of the earth?

  1. What is the speed that a person in Yellowknife is moving due to the rotation of the earth?