Assignment #5.02: Friction

1. A man pushes a 5 kg box with a force of 20 N. The box accelerates at a rate of 1 m/s2.
  1. What is the force of friction on the box?

  1. What is the coefficient of friction between the box and the floor?

You are pulling a 5 kg mass with a force of 15 N just before it starts moving. What is the coefficient of static friction?

You are designing a bulldozer for the moon, and estimate the coefficient of friction for pushing lunar soil across the moon's surface to be 0.55. What is the minimum force that the engine should be able to exert to cause an acceleration of 0.25 m/s2 for 2000 kg of lunar soil across a level part of the lunar surface? (On the moon, g=1.67 m/s2)

A 5 kg box is sliding across the floor with a velocity of 4 m/s. mk is 0.25. How far does the box go before coming to a stop?

1. A 700 kg car is coasting down a 45° slope. Its acceleration is 2.5 m/s2.
  1. What is the force of gravity on the car?

  1. What is the component force of gravity pulling the car down the hill?

  1. What is the normal force acting on the car?

  1. What is the force of friction on the car?

  1. What is the coefficient of friction for the car?

You place an object, of mass m on a tabletop. The table is then tilted to an angle of q, where the object just overcomes friction and begins to slide. Prove that ms = tan (q). Be sure that you include a free-body diagram.

1. In the sport of curling, a stone is slid across a 46-meter long ice lane. The coefficient of kinetic friction between the ice and the rock is 0.017. The mass of the stone is 20 kg, and its initial speed is 4 m/s.
  1. What is the force of friction on the stone?

  1. What is the acceleration of the stone due to friction?

  1. What is time it takes for the stone to reach the end of the lane?

  1. What is the final speed of the stone?