Experiment 9:
Latent Heat of Vaporization

Background:
In order for a material to change phases, energy must be added to the material. This energy is called the Latent Heat. In this experiment, the Latent Heat of Vaporization is determined for Water. It is compared to the statndard value of 2.26 x 106 J/kg.

Materials you will need:
Hot Plate
Thermometer
Pyrex or other heat-resistant glass Beaker
Water
Stopwatch

Instructions:
Turn on the hot plate to medium-high heat (setting 4 or 5). Allow the hot plate to pre-heat for about 5 minutes.

While the hot plate is heating, measure the mass of the empty beaker. Then, pour 200 mL of water into the beaker, and measure the total mass of the water and beaker. Calculate the mass of the water. (Pure water should be 200g. Tap water has dissolved minerals in it, and thus should have a slightly greater mass.) Record the initial temperature of the water using a thermometer.

After the hot-plate has been pre-heated, place the beaker on the hot-plate. Put the thermometer into the water, and leave it immersed for the duration of the experiment. When the temperature reaches 80ºC, start the timer. Stop the timer when the temperature reaches 90ºC. This will be used later to determine the energy entering the water per unit time.

When the water begins to boil (In El Paso, this will likely be around 97ºC, depending on atmospheric pressure and other factors), start the timer again.