Assignment 2: Gauss's Law
A 30 meter long plastic cylinder has a radius of 10 cm, as shown below. It has a linear charge density of 0.25 C per meter.

  1. Calculate the total charge of the cylinder.

  1. Calculate the electric field inside the cylinder, 15 meters from the end of the cylinder, at a radius of 4 cm.

  1. Calculate the electric field outside the cylinder, 10 meters below the center of the cylinder.

1. A hollow metal sphere has an internal radius of 0.5 m, and an external radius of 0.6m, as shown in the diagram. A change of -0.5C is placed on the sphere.

  1. What is the external surface area of the sphere?

  1. What is the charge density at the surface of the sphere?

  1. What is the electric field at r =0.1 m?

  1. What is the electric field at r = 0.55 m?

  1. What is the electric field at r = 0.75 m?

λ = 0.01 C/m

A thin, infinitely long wire has a charge density of 0.01 C / m. Calculate the electrical field a distance of 10 centimeters above the wire.

1. A 1-cm radius glass marble has a charge of +Q. It is placed inside a conducting sphere, with internal radius 10 cm and external radius of 12 cm.
  1. Derive an expression for the electric field inside the glass marble.

  1. Derive an expression for the electrical field between the marble and the conducting sphere.

  1. Derive an expression for the electric field inside the conducting sphere.

  1. Derive an expression for the electric field outside the conducting sphere.

1. A thin wire, with charge density 1 mC/m is placed in the center of a thin pipe of radius 1 cm. The pipe and wire are both 40 m long.
  1. Derive and expression for the electric field between the wire and the pipe.

  1. The pipe is grounded, and excess electrons flow into the pipe until the pipe contains a complete “mirror charge” for the wire. Calculate the charge density (σ)of the pipe.