Assignment #5.03:Elevators
1. Fabian has a mass of 70 kg.
  1. What is his weight due to the earth’s gravity?

  1. He gets into an elevator that accelerates upward at 4 m/s2. What is his apparent weight inside the elevator.

  1. At the top of the building, he realizes that he got off on the wrong floor, and rides the elevator back down. If the elevator accelerates at 4 m/s2 downward, what is his apparent weight?

1. Evelyn is standing on a scale inside an elevator. When the elevator is not moving, the scale reads 500N.
  1. What will the scale read when the elevator is accelerating upward at 6 m/s2?

  1. What will the scale read when the elevator is accelerating downward at 4 m/s2?

1. Jennifer is on Mars (gmars = 3.72 m/s2), where her spaceship is about to take off. Jennifer’s mass is 45 kg.
  1. What is Jennifer’s weight on earth?

  1. What is Jennifer’s weight on mars?

  1. What is Jennifer’s apparent weight as her spaceship accelerates upward at 17 m/s2?

1. Gale is going to work in a coal mine. He rides an elevator that has two cars, connected via a pulley. The mass of the empty car is 1500 kg, and the mass of the loaded car is 1600 kg. As the car begins to move, there is a blackout, and the motor driving the elevator disengages, allowing the elevator-pulley system to move freely.
  1. What is the acceleration of the elevator car?

  1. What is Gale's apparent weight?

Anabel has a mass of 65 kg. She is riding a roller coaster that accelerates upward at 22.5 m/s2. What is her apparent weight?

1. If you were to go to Jupiter, which of the following would be true? (Choose Two)
  1. Your mass would remain about the same.
  2. Your weight would remain about the same.
  3. Your mass would increase.
  4. Your weight would increase.

1. When you ride in an airplane, which of the following would be true? (Choose Two)
  1. Your mass would remain about the same.
  2. Your weight would remain about the same.
  3. Your mass would increase.
  4. Your weight would increase.

1. When you eat a large Thanksgiving Dinner, which of the following would be true (Choose Two)
  1. Your mass would remain about the same.
  2. Your weight would remain about the same.
  3. Your mass would increase.
  4. Your weight would increase.