Experiment 4:
Polarization of Light
Background:
Light is often described as an electromagnetic wave. Waves can be polarized – that is, the direction of their vibration can be controled. In this experiment, two polarizing filters are used to verify the relationship between the angle between two polarizers (θ) and the intensity of the light before and after a polarizer. (I1 and I2). The equation to be verified is:
I sub 2 = I sub 1 sin^2( θ ) (1)

Materials you will need:
A light source (Mini Flashlight)
Galvanometer
Wires
Dark enclosure with Photovoltaic Cell.
Protractor

Experimental Setup:

Flashlight

hole

Polarizer

Galvanometer

Enclosure

Polarizer

Photovoltaic
Cell

*In this experiment, the polarizers, enclosure, and photovoltaic cell are all part of the enclosure assembly. Do not attempt to take this assembly apart.

Procedure:
1. Place the enclosure/polarizer assembly open-side down on a flat surface.

2. Connect the galvanometer to the two wires of the enclosure assembly.

3. There is a small tick-mark on the outside polarizer. Rotate the polarizer until the tick mark aligns with 90 degrees.

4. Shine the flashlight through the polarizer and verify that there is a reasonable reading on the galvanometer Somewhere between 20 and 50 mA.

5. Rotate the polarizer to 0 degrees. Shine the flashlight through the polarizer and record the angle and the reading on the galvanometer.

6. Rotate the polarizer to 10 degrees. Shine the flashlight through the polarizer and record the angle and the reading on the galvanometer.

7. Repeat step 6, increasing the angle by 10 degrees at a time until you have readings for a complete circle.

8. Graph your data both in a calculator and by hand on paper. Verify that your data fits the equation I sub 2 = I sub 1 sin^2( θ ) .