9 Weeks' Test
1. Which of the following quantities is not a vector?
  1. Electric Field
  2. Magnetic Field
  3. Electric Potential
  4. Force
  5. velocity

1. Consider four charges, A, B, C and D, that exist in a region of space. Charge A attracts charge B, but B repels C. C repels D and D is positively charged. What is the sign of the charge A?
  1. Positive
  2. Negative
  3. Neutral
  4. All of the charges are positive.
  5. All of the charges are negative.

1. A proton is traveling to the left through a magnetic field that is directed into the page. The force on the proton is -
  1. toward the top of the paper
  2. toward the bottom of the paper
  3. toward the left side of the paper
  4. toward the right side of the paper
  5. into the paper.

1. A wire carries an unknown amount of current, I. The magnetic field at a fixed distance from the wire is measured to be 0.3 T. A short time later, the magnetic field is measured to be 0.6 T. The current in the wire is now -
  1. I/4
  2. I/2
  3. I
  4. 2I
  5. It cannot be determined from the information provided.

1. A capacitor has a capacitance of 2 mF. If the area of the plates were doubled, and the separation between the plates was halved, what would the new capacitance be?
  1. 0.5 mF
  2. 1 mF
  3. 2 mF
  4. 4 mF
  5. 8 mF

1. Two parallel conducting plates are connected to a constant voltage source. The magnitude of the electric field between the plates is 2,000 N/C. If the voltage is doubled and the distance between the plates is reduced to 1/5 the original distance, the magnitude of the new electric field is
  1. 800 N/C
  2. 1,600 N/C
  3. 2,400 N/C
  4. 5,000 N/C
  5. 20,000 N/C

1. A rectangular wire loop is at rest in a uniform magnetic field B of magnitude 2 T that is directed out of the page. The loop measures 5 cm by 8 cm, and the plane of the loop is perpendicular to the field, as shown above. The total magnetic flux through the loop is
  1. zero
  2. 2 x 10-3 Tm2
  3. 8 x 10-3 Tm2
  4. 2 x 10-1 Tm2
  5. 8 x 10-1 Tm2