Assignment #5.03:Elevators and Pulleys
1. Fabian has a mass of 80 kg.
  1. What is his weight due to the earth’s gravity?

  1. He gets into an elevator that accelerates upward at 4 m/s2. What is his apparent weight inside the elevator.

  1. At the top of the building, he realizes that he got off on the wrong floor, and rides the elevator back down. If the elevator accelerates at 4 m/s2 downward, what is his apparent weight?

1. Evelyn is standing on a scale inside an elevator. When the elevator is not moving, the scale reads 560N.
  1. What will the scale read when the elevator is accelerating upward at 6 m/s2?

  1. What will the scale read when the elevator is accelerating downward at 4 m/s2?

1. Jennifer is on Mars (gmars = 3.72 m/s2), where her spaceship is about to take off. Jennifer’s mass is 65 kg.
  1. What is Jennifer’s weight on earth?

  1. What is Jennifer’s weight on mars?

  1. What is Jennifer’s apparent weight as her spaceship accelerates upward at 12 m/s2?

1. A pulley is hung from the ceiling. The left side of the pulley is connected to a 7 kg mass. The right side of the pulley is connected to a 10 kg mass.
  1. What is the acceleration of the system?

  1. What is the tension in the rope?

1. Gale is going to work in a coal mine. He rides an elevator that has two cars, connected via a pulley. The mass of the empty car is 1600 kg, and the mass of the loaded car is 1700 kg. As the car begins to move, there is a blackout, and the motor driving the elevator disengages, allowing the elevator-pulley system to move freely.
  1. What is the acceleration of the elevator car?

  1. What is Gale's apparent weight?

1. An 11 kg block is on top of a table. The coefficient of kinetic friction between the table and the block is 0.3. It is connected to a rope that passes over a pulley at the end of the table. The rope hangs off the table and is connected to a 5 kg mass, as shown in the diagram.
  1. What is the force of friction on the 11 kg block?

  1. What is the acceleration of the system.

  1. What is the tension in the rope?