Definition of average velocity		v sub avg equiv Δd over Δt
Definition of average acceleration		a equiv Δv over Δt = {v sub f - v sub i} over Δt
Kinematic Equations		v sub avg = {v sub i + v sub f } over 2
		v sub f = v sub i + a Δt
		Δd = v sub i Δt + 1 over 2 a Δt^2
		v sub f ^2 = v sub i ^2 + 2 a Δd
Newton's Second Law		vec F = m vec a
Force of Friction		F sub f = μ F sub N
Work		W equiv vec F cdot vec d = F d cos θ
Power		P equiv ΔE over Δt = W over Δt = F v cos θ
Gravitational Potential Energy		U sub g = m g h
Kinetic Energy		K = 1 over 2 m v ^2
Conservation of Energy		U sub i + K sub i + W = U sub F + K sub f
Force of a Spring		F sub s = - k x
Elastic Potential Energy		U sub s = 1 over 2 k x^2
Period of a Spring		T sub s = 2 π sqrt {m over k}
Impulse		vec J = vec F t
Momentum		vec p = m vec v
Conservation of Momentum		vec p sub i + vec J = vec p sub f
Period of a Pendulum		T sub p = 2 π sqrt {g over L}
Centripetal Acceleration		a sub c = v ^2 over r
Centripetal Force		F sub c = {m v^2 }over r
Universal Gravitation		F sub g = {G m sub 1 m sub 2} over r ^2
Kepler's Laws	1st Law: Eccentricity	ε = {r sub max - r sub min} over { r sub max + r sub min}
	2nd Law: Equal Areas in Equal Time	ΔA over Δt = 1 over 2 r sub 1 v sub 1 = 1 over 2 r sub 2 v sub 2
	3rd Law: Orbital Period and average orbital radius	(T sub 1) ^2 over (r sub 1 )^3 = (T sub 2) ^2 over (r sub 2)^3
Frequency and Period		f = 1 over T
Velocity of a Wave		v = f λ
Doppler Shift for Sound		f' = f ({v +- v sub o} over {v +- v sub s})
Index of Refraction		n equiv c over v sub m
Snell's Law		n sub i sin %theta sub i = n sub r sin %theta sub r
Resistors in Series		R sub eq = sum from { { i = 1 } } to { n } R sub i = R sub 1 + R sub 2 + R sub 3 +... + R sub n
Resistors in Parallel		R sub eq = 1 over sum from { { i = 1 } } to { n } {1 over R sub i} = 1 over {1 over R sub 1 + 1 over R sub 2 + 1 over R sub 3 +... + 1 over R sub n}
Ohm's Law		V = I R
Definition of Resistance		R = {ρ L} over A
Electrical Power		P = I V = I^2 R = V^2 over R

Constants:

g sub earth = 9.81 m/s^2

G = 6.67 x 10^-11 {N m^2 } over kg^2