Assignment 7: Rotational Motion II

1. A 75 kg man stands on a 5 meter long platform suspended by one cable at each end. He is 2 meters from the left side. The mass of the platform is 10 kg. The cable on the right side of the platform breaks.
  1. Calculate the angular acceleration of the platform.

  1. If the man can catch the platform when it has rotated 45 degrees, what is the time he has to react?

2. A 15 m long hose is initally spooled around a reel that is initially at rest. The moent of inertia of the reel is 0.44 kg m2. Its radius is 0.16 m. When the reel is turning, a frictional torque of magnitude 3.4 m´N acts on the wheel. IF the hose is pulled so that the tension in the hose is a constant 25N, how long does it take to unwind the hose from the reel?

A bicycle is placed upside down during a maintanence check. The front wheel (m=1.3 kg) is allowed to spin at a rate of 4 revolutions per second. The wheel has a radius of 0.33 m. The brake is then applied to the wheel, and the wheel comes to a stop in 2.5 seconds. What is the torque that was applied to the wheel. (assume the wheel is a hoop or ring and the mass of the spokes is negligible.)

1. The mass of the earth is 5.974 x 1024 kilograms. Its radius is 6.387 x 106 m. The moment of inertia for a solid sphere is given by I = {2 over 5} m r^2 . The earth rotates once every 24 hours.
  1. What is the rotational velocity of the earth (in radians per second)?

  1. What is the Moment of Inertia of the earth?

  1. What is the rotational kinetic energy of the earth?

1. The moon orbits the earth approximately once every 28 days. Its mass is 7.36 x 1022 kg, and its orbit is in the same direction as the earth's rotation.
  1. What is the orbital radius of the moon?

  1. What is the total angular momentum of the earth-moon system?

  1. The moon is moving away from the earth at 0.038 meters per year. How far will the moon be from the earth after 1 Billion years?

  1. Use the law of conservation of angular momentum to calculate the length of a day on earth 1 billion years from now.