Assignment 5: Capacitors
Multiple Choice:
1. A capacitor has plates that are each 2 m2. The distance between the plates is 1 x 10-4 m. A voltage of 20 V is applied to the capacitor. What is the strength of the electric field between the plates of the capacitor?
  1. 1.771 x 10-7 V/m
  2. 3.542 x 10-6 V/m
  3. 1 x 104 V/m
  4. 2 x 105 V/m
  5. There is no electric field inside the capacitor.

1. A capacitor is connected to a 12 Volt battery and allowed to charge. The capacitor is then disconnected from the battery. Using insulated scissors, each plate of the capacitor is cut in half, and two new capacitors are formed, each storing half of the original charge. The plates in each of the new capacitors are separated by the same distance as the original capacitor. What is the new voltage of each of the new capacitors?
  1. 48 V
  2. 24 V
  3. 12 V
  4. 6 V
  5. 3 V

1. A capacitor has a capacitance of 3.2 x 10-6 F. If a 2 volt potential difference is applied to the capacitor, what is the charge that the capacitor will store when fully charged?
  1. 6.25 x 105 C
  2. 6.4 x 10-6 C
  3. 3.2 x 10-6 C
  4. 1.6 x 10-6 C
  5. 0 C

1. A capacitor is a device that -
  1. Stores energy in an electric field.
  2. Stores energy in a magnetic field.
  3. Stores energy in a gravitational field.
  4. Dissipates energy as heat.
  5. None of the above.

Multiple Correct:
In the following question, two answer choices are correct. Circle BOTH of the correct choices. No credit will be given for incorrect or partially correct answers.
1. A capacitor is filled with oil (e = 6.5), and has a capacitance of 0.02 F. It is connected to a 1.5 Volt battery. Which of the following changes to this capacitor would allow it to store more charge?
  1. Reducing the size of the plates in the capacitor.
  2. Changing the battery to a 6 V battery.
  3. Increasing the spacing between the plates.
  4. Draining the dielectric oil and replacing it with plastic (e = 9)
  5. Placing the capacitor in a strong magnetic field.

1. A capacitor is constructed using two pieces of aluminum foil and a piece of Wax-paper. The wax-paper has a dielectric constant of 4.75. All three objects have an area of 0.01 m2 and a thickness of 4 x 10-4 m.
  1. Draw a diagram of how the capacitor should be constructed.

  1. Assuming that the capacitor is constructed perfectly, calculate the expected capacitance of the capacitor.

  1. You wish to use the capacitor to store a charge of 2 mC. What is the voltage you will need to apply to the capacitor in order to achieve this?