Assignment 6.05: Springs and Elastic Potential Energy

1. Lance has a spring with a spring constant of 500 N/m. He hangs the spring from the ceiling and pulls down on it, stretching it 0.4 meters.
  1. What is the force that the spring exerts on his hand?

  1. Is the force up or down?

  1. What is the energy stored in the spring?

1. Ashley drives her car over a speed bump, causing a spring in her car's shock-absorbing system to be compressed a distance of 0.2 meters. The force exerted on the spring is 3000 N.
  1. What is the spring constant for this spring?

  1. What is the energy that is stored in this spring?

1. Shin-Hae attaches a spring to a wall, and pulls on the spring with a force of 255 N. The spring has a spring constant of 1000 N/m.
  1. What is the distance the spring stretches?

  1. What is the energy stored in the spring?

1. Eunice stretches a rubber band a distance of 0.18 m. The rubber band stores a potential energy of 1.2 J.
  1. What is the spring constant of the rubber band?

  1. What is the force that the rubber band is exerting on her hand?

1. A spring-based jumping toy has a mass of 1 gram, as shown in the picture. It is compressed a distance of 2 cm, where a suction cup momentarily holds it in place. When the suction cup releases, the toy “jumps” to a height of 0.56 meters.
  1. What is the gravitational potential energy the toy has at the top of its path?

  1. What is the elastic potential energy that was stored in the spring before the toy “jumped”?

  1. What is the spring constant?

Lucas has a mass of 65 kg. He lies down on his bed to take a nap, compressing 15 springs in his bed equally. If his weight is distributed equally on each spring, and all the springs in his bed have a spring constant of 1015 N/m, how far is each spring compressed?

Christopher uses a Nerf® gun to shoot Manuel. He pulls back on the “hammer”, causing a spring to compress a distance of 0.11 meters. The mass of a Nerf® dart is 0.002 kg. The final velocity of the dart is 4.3 m/s. Use the law of conservation of energy to calculate the spring constant of the spring inside the Nerf® gun.