Assignment #11.01: Refraction
Light travels at 1.6 x 108 m/s in a certain type of material. What is the index of refraction of the material?

1. A ray of light travels from air (n=1) to water (n=1.33). It is incident at an angle of 20 degrees from the normal.
  1. What is the speed of light in the water?

  1. Draw a diagram of the situation.

  1. What is the angle that the refracted ray leaves the interface with?

A dolphin looks up and sees the sun at an angle of 15 degrees from the normal, as shown in the diagram. What is the actual angle of the sun from the normal?
Air (n=1)
Water (n=1.33)

A fiber optic cable is a thin glass wire (n=1.6) coated with a plactic “jacketing” (n=1.4). What is the critical angle for a fiber optic cable?

1. Light goes from diamond (n=2.417) to air (n=1).
  1. What is the critical angle for the diamond/air interface?

  1. The diamond is then placed in water (n=1.33). What is the new critical angle?

  1. When will the diamond reflect more light due to total internal reflection – in water or in air? Justify your answer.

A ray of light goes through several materials, as shown in the diagram. The original angle of incidence is 15 degrees. Find the angle of the final refracted ray of light.

Water (n=1.33)
Air (n=1)
Plastic (n=1.25)
Water (n=1.33)
Glass (n=1.6)
Plastic (n=1.25)
air (n=1)
Glass (n=1.6)