Assignment #8: Light and Energy

A laser-pointer has a wavelength of 650 nm. Its power is 50 mW. How many photons does the laser emit in one second?

1. Sunlight at 1 AU (1 Astronomical Unit = the average distance between the earth and the sun) from the sun an average intensity of 1361 W/m2. Its average wavelength is 500 nm. A solar sail, in earth orbit, has an area of 100 m2. The sail is painted perfectly black, so that all light that falls on it is absorbed.
  1. Calculate the energy of an average photon of sunlight.

  1. Calculate the momentum of one photon of sunlight.

  1. Calculate the number of photons that strike the solar sail in one second.

  1. Calculate the total momentum transfered to the sail in one second.

  1. What is the total force that the solar sail feels due to sunlight?

A nuclear bomb destroys approximately 3 grams of material. What is the total energy released in a nuclear explosion?

1. An amateur radio operator in El Paso sends a 100W signal to a station in Hawaii, using a frequency of 28.350 MHz. The transmission lasts 35 seconds.
  1. What is the energy of a single photon?

  1. What is the number of photons that are radiated by the antenna?

  1. What is the momentum of a single photon?

  1. What is the total momentum of all the photons that are sent to the station in Hawaii?

1. A commercial radio station transmits a radio signal on 102.1 MHz, using a power of 186 KW for 24 hours.
  1. What is the energy of a single photon?

  1. What is the number of photons that are radiated by the antenna?

  1. What is the momentum of a single photon?

  1. What is the total momentum of all the photons that are transmitted?

  1. Why doesn’t the broadcasting tower fall over?