Assignment 3: Capacitors
1. Which of the following actions would increase the energy stored in a parallel-plate capacitor? (Circle All that apply)
  1. Increasing the area of the plates
  2. Decreasing the area of the plates
  3. Increasing the separation of the plates
  4. Decreasing the separation of the plates
  5. Inserting a dielectric between the plates.

What is the capacitance of a capacitor that stores a 4.3 mC charge when a voltage of 1.5 V is applied to the capacitor?

1. A capacitor is made from two circular plates, each of radius 4.3 m. They are separated by a layer of oil with a thickness of 0.01 m. The dielectric constant for the oil is 6.7. What is expected capacitance of the capacitor?

An air-filled, parallel-plate capacitor has a capacitance of 2 x 10-4 F. The separation between the plates of the capacitor is 5 x 10-4 m. What is the area of each plate?

The electrical potential energy stored in a defibrillator capacitor is 75 J. Its capacitance is 120 mF. What is the Voltage of the capacitor when it is fully charged?

A Parallel plate capacitor has a capacitance of 7 mF, and is filled with an unknown dielectric. The area of each plate is 1.5 m2, and the separation between the plates is 1 x 10-5 m. What is the dielectric constant of the dielectric?

Two identical capacitors store different amounts of charge. Capacitor A stores 2 x 10-5 C. Capacitor B stores 6 x 10-5 C. If the voltage of capacitor A is 3 V, what is the voltage of capacitor B?

An empty parallel-plate capacitor is connected to the terminals of a 9V battery and allowed to fully charge. The capacitor is disconnected from the battery, and the spacing between the plates is doubled. As a result of this change, what is the new voltage between the plates of the capacitor?

Two capacitors have the same plate separation, but one has square splates and the other has circular plates. The spare plates are a length L on each side, and the diameter of the circular plates is L. The capacitors have the same capacitance because they contain different dielectric materials. The dielectric constant of the material between the square plates has a value of e = 3. What is the dielectric constant of the material between the circular plates?