Assignment 4: Magnetic Fields and Wires

What are the three elements that are ferromagnetic?

What causes magnetic fields to be generated?

1. Draw a diagram of a current-carrying wire and the magnetic field due to the wire in each of the following situations:
  1. A long wire carries current to the left.

  1. A long wire carries current toward the top of the page.

  1. A long wire carries current into the page.

A wire carries a current of 25 A to the left. Calculate the magnetic field at a point 2 cm toward the bottom of the page from the wire.

The magnetic field due to a long wire carrying current is 0.2 T at a distance of 1 cm from the wire. What would the magnetic field be at a distance of 4 cm from the wire?

1. The magnetic field due to a long wire that is carrying current to the right is 0.25 T at a point 7 cm toward the top of the page.
  1. What is the direction of the magnetic field?

  1. What is the magnitude of the current in the wire?

1. Power lines can sometimes carry a current of 1000 Amps.
  1. What would the magnitude of the magnetic field of one of these power lines be at a distance of 1 cm?

  1. What would the magnitude of the magnetic field of one of these power lines be at a distance of 1 m?

1. A Magnetar is a type of neutron star that has an extremely strong magnetic field – they are the most magnetic objects in the universe. If a magnetar were to replace our sun, the magnetic field of the magnetar would strip all information from every magnetic stripe on every credit card on the Earth. A magnetar's magnetic field can be as strong as 1x1011 T at its surface, a distance of 20 km from an area of plasma-ion circulation near its core.
  1. If this magnetic field were due to charged protons moving in a straight line, how much current would be required to produce a magnetic field of this strength.