Assignment 4.01: Resistors and Resistivity
Material	Resistivity (Ωm)
Carbon (Graphite)	1x10-5
Copper	1.7x10-8
Germanium	4.6x10-1
Gold	2.4x10-8
Iron	1x10-7
Lead	1.9x10-7
Platinum	9.8x10-8
Silicon	6.4x10-2
Silver	1.6x10-8
Steel	6.9x10-7
Tungsten	4.9x10-8

A carbon rod is 10 cm long and has a diameter of 0.9 mm. What is the resistance of the rod?

1. In late 2008, the world’s longest power cable was switched on. The cable stretches 580 km from Feda in Norway across the North Sea to Eemshaven in the Netherlands and uses a voltage of 1,500 kV. It has a diameter of 7.62 centimeters and is made of steel (iron).
  1. What is the resistance of the cable?

  1. What is the amount of current that flows in the cable.

You measure the resistance of a tungsten filament of a light bulb to be 240 Ohms. If the filament has a diameter of 0.046 mm, what is the length of the filament?

1. You wish to design a circuit that wastes as little energy as possible as heat.
  1. What material should you make the wires out of? Explain why.

  1. Should you use thicker wires or thinner wires? Explain why.

  1. Should wire length be minimized or maximized? Explain why.

A rheostat is a type of variable resistor in which a long wire is wrapped around a core. A slider then touches the wire and can be moved along a line, as seen in the photo. In a well-written paragraph, explain how this device can have a variable resistance.