Experiment 9:
Latent Heat of Vaporization

Background:
In order for a material to change phases, energy must be added to the material. This energy is called the Latent Heat. In this experiment, the Latent Heat of Vaporization is determined for Water. It is compared to the standard value of 2.26 x 106 J/kg.

Materials you will need:
Hot Plate
Thermometer
Stopwatch
Pyrex or other heat-resistant Erlenmeyer flask.
Water
Forceps
Watch Glass

Instructions:
Turn on the hot plate to high heat. Allow the hot plate to pre-heat for about 5 minutes.

While the hot plate is heating, measure the mass of the empty flask. Then, pour 200 mL of water into the flask, and measure the total mass of the water and flask. Calculate the mass of the water. (Pure water should be 200g. Tap water has dissolved minerals in it, and thus may have a slightly greater mass.) Record the initial temperature of the water using a thermometer.

After the hot-plate has been pre-heated, place the flask on the hot-plate. Put the thermometer into the water, and leave it immersed for the duration of the experiment. Place a watch-glass over the top of the flask to minimize evaporative losses of the water before it begins to boil. When the temperature reaches 40ºC, start the timer. Stop the timer when the temperature reaches 80ºC. This will be used later to determine the energy entering the water per unit time.

When the water temperature stabilizes, and the begins to boil (In El Paso, this will likely be around 98ºC, depending on atmospheric pressure and other factors), remove the watch glass from the top of the flask and start the timer again. Allow the water to boil for 5 minutes. Using forceps or an oven mitt, remove the flask from the hot plate, and measure the new mass of the flask and water. Calculate the mass of the water remaining, and the change in mass of the water.

Use Q = mcΔT and P = E/T to calculate the Power (rate that energy is transferred into the water) of the hot-plate.

Calculate the amount of energy that was transferred during the 5 minutes the water was boiling.

Calculate the Latent Heat of Vaporization for water.