Definition of average velocity		v sub avg = d over t
Definition of average acceleration		a = Δv over t = {v sub f - v sub i} over t
Kinematic Equations		d = ({v sub i + v sub f } over 2)t Or (x - x_0) =( {v sub 0 + v } over 2)t
		v sub f = v sub i + a t Or v = v sub 0 + a t
		d = v sub i t + 1 over 2 a t^2 Or x = x sub 0 + v sub 0x t + 1 over 2 a sub x t^2
		v sub f ^2 = v sub i ^2 + 2 a d Or v ^2 = v sub 0 ^2 + 2 a ( x-x sub 0 )
Trigonometric Functions		sin( θ ) = opp over hyp
		cos( θ ) = adj over hyp
		tan( θ ) = opp over adj
Newton's Second Law		vec F = m vec a
Force of Friction		F sub f = μ F sub N
Work		W equiv vec F cdot vec d = F d cos θ
Power		P equiv ΔE over Δt = W over Δt = F v cos θ
Gravitational Potential Energy		U sub g = m g h
Kinetic Energy		K = 1 over 2 m v ^2
Conservation of Energy		U sub i + K sub i + W = U sub F + K sub f
Force of a Spring		F sub s = - k x
Elastic Potential Energy		U sub s = 1 over 2 k x^2
Period of a Spring		T sub s = 2 π sqrt {m over k}
Period of a Pendulum		T sub p = 2 π sqrt {L over g}
Impulse		vec J = vec F t
Momentum		vec p = m vec v
Conservation of Momentum		vec p sub i + vec J = vec p sub f
Center of Mass		x sub { CM} = { x sub 1 m sub 1 + x sub 2 m sub 2 ...} over { m sub 1 + m sub 2 ... }
Centripetal Acceleration		a sub c = v ^2 over r
Centripetal Force		F sub c = {m v^2 }over r
Arc length		s = r θ
Linear / Angular Velocity Relationship		v = r ω
Linear / Angular Acceleration Relationship		a = r α
Definition of Average Angular Velocity		ω sub avg equiv θ over t
Definition of Angular Acceleration		α equiv Δω over t = {ω sub f - ω sub i} over t
Angular Kinematic Equations		ω sub avg = {ω sub i + ω sub f } over 2
		ω sub f = ω sub i + α t
		θ = ω sub i t + 1 over 2 α t^2
		ω sub f ^2 = ω sub i ^2 + 2 α θ
Torque		vec τ = vec r times vec F
Newton's Second Law (Rotational)		vec τ = I vec α
Angular Momentum		vec L = I vec ω
Universal Gravitation		F sub g = {G m sub 1 m sub 2} over r ^2
Kepler's Laws	1st Law: Eccentricity	ε = {r sub max - r sub min} over { r sub max + r sub min}
	2nd Law: Equal Areas in Equal Time	A sub 1 over T sub 1 = A sub 2 over T sub 2 Or r sub 1 v sub 1 = r sub 2 v sub 2
	3rd Law: Orbital Period and average orbital radius	{T sub 1} ^2 over {R sub 1 }^3 = {T sub 2} ^2 over {R sub 2}^3
Frequency and Period		f = 1 over T
Velocity of a Wave		v = f λ
Constructive Interference		d sin %theta = n λ
Destructive Interference		d sin %theta = (n + 1 over 2) λ
Resonance (both open or closed)		L = {n λ} over 2
Resonance (One side open)		L = { n λ} over 4 Where n is odd
Doppler Shift for Sound		f sub o = f sub s ({v +- v sub o} over {v +- v sub s})
Index of Refraction		n equiv c over v sub m
Snell's Law		n sub i sin %theta sub i = n sub r sin %theta sub r
Lens Equation		1 over f = 1 over o + 1 over i
Resistors in Series		R sub eq = sum from { { i = 1 } } to { n } R sub i = R sub 1 + R sub 2 + R sub 3 +... + R sub n
Resistors in Parallel		R sub eq = 1 over sum from { { i = 1 } } to { n } {1 over R sub i} = 1 over {1 over R sub 1 + 1 over R sub 2 + 1 over R sub 3 +... + 1 over R sub n}
Ohm's Law		V = I R
Definition of Resistance		R = {ρ L} over A
Electrical Power		P = I V = I^2 R = V^2 over R

Constants:

g sub earth = 9.81 m/s^2

G = 6.67 x 10^-11 {N m^2 } over kg^2

c = 2.998 times 10^8 m/s approx 3 times 10^8 m/s

v sub sound approx 343 m/s