Assignment #1: Thermodynamics I
An object is insulated from its enviornment, such that no heat can flow into or out of the object. Can the temperature of the object change? If so, give an example.

The second law of thermodynamics states that it is impossible to convert 100% of heat that leaves a hot reservoir into work. Is the converse statement true (Is it possible to convert 100% of a given amount of mechanical work into heat?) Explain your answer.

Humpty Dumpty sat on a wall. Humpty Dumpty had a great fall. All the King's Horses and all the King's men couldn't put Humpty together again. Which law of thermodynamics is most applicable? (Circle One)

Zeroth Law	First Law	Second Law

1. A heat engine operates with a hot temperature of 50°C and a cold temperature of 20°C.
  1. What is the efficiency of the engine?

  1. Both temperatures are doubled. What is the efficiency of the engine now? (*Hint: What does it mean to double a temperature?)

1. A heat engine performs 2700J of work, and has an efficiency of 18%.
  1. How much energy was taken from the hot reservoir?

  1. How much heat was lost to the cold resevoir?

  1. If the efficiency of the engine is increased, do parts (a) and (b) increase, decrease, or stay the same?

1. To keep a room at a comfortable 21°C, a heat pump does 345 J of work. It supplies the room with 3240J of heat.
  1. How much heat is removed from the outside air by the heat pump?

  1. What is the temperature of the outside air?

1. A power plant produces 500 megawatts of power by producing steam at 400°C. It cools the steam in a river, that is 30 meters wide, and 20 meters deep, flowing at 2 m/s. Before encountering the power plant's pipes, the river water is 13°C.
  1. What is the maximum possible efficiency of the power plant?

  1. What amount of power leaves the hot reservoir?

  1. What amount of power is lost to the river?

  1. What is the temperature of the river water after it passes the cooling coils?