Assignment #5: Electric Fields and Capacitors

1. Two places of metal are separated by a distance of 1 mm. Each of the plates has a surface area of 0.5 m2. The plates are separated by empty space.
  1. What is the capacitance of the capacitor?

  1. What is the charge that builds up on the capacitor if a voltage of 120 V is applied?

1. An electron is placed in between two plates of a capacitor. The capacitor’s capacitance is 0.130 Farads. The plates are separated by a distance of 0.25 cm, and the capacitor is charged to 15 Volts.
  1. What is the magnitude of the electric field inside the capacitor?

  1. What is the force felt by the electron?

  1. What is the acceleration of the electron?

  1. How long does it take the electron to travel across the capacitor?

1. The bottom of a thunderstorm is approximately 3000 m above the surface of the earth. It has a charge of -4C. The earth forms a “mirror” charge of +4C. The thunderstorm covers an area of 400 km2.
  1. What is the electric field in the region between the thunderstorm and the earth?

  1. What is the Capacitance of this region?

1. A Cathode-Ray tube has a voltage of 500V between a metal plate and a grid, separated by a distance of 0.015 m.
  1. What is the Electric Field between the plate and grid?

  1. An electron is placed inside the region of electric field. What is the potential energy of the electron?

  1. What is the Force on the electron in this region?

  1. What is the final kinetic energy of the electron?

  1. What is the final velocity of the electron?

  1. How long would it take the electron to travel 30 cm to the front of CRT?